Introduction to Highly Available NFS Server on scale-out storage systems based on GlusterFS
Soumya Koduri
Red Hat
Meghana Madhusudhan
Red Hat

---
AGENDA
- What is GlusterFS?
- Integration with NFS-Ganesha
- Clustered NFS
- Step-by-step guide
- Future Directions
- Q&A

---
GlusterFS

---
GlusterFS
- An open source, scale-out distributed file system
- Software Only and operates in user-space
- Aggregates Storage into a single unified namespace
- No metadata server architecture
- Provides a modular, stackable design
- Runs on commodity hardware
[Speaker Notes: * aggregates various storage servers over Ethernet or Infiniband RDMA interconnect into one large parallel network file system * uses any ondisk file system which supports extended attributes (eg: ext4, XFS, etc) to format to store data on disks]

---
Architecture
- Data is stored on disk using native formats (e.g. ext4, XFS)
- Has client and server components
    - Servers, known as storage bricks (glusterfsd daemon), export local filesystem as volume
    - Clients (glusterfs process), creates composite virtual volumes from multiple remote servers using stackable translators
    - Management service (glusterd daemon) manages volumes and cluster membership

---
GlusterFS Deployment

---
Access Mechanisms
- FUSE based Native protocol
- NFSv3
- libgfapi
- ReST/HTTP
- HDFS

---
libgfapi
- A user-space library with APIs for accessing Gluster volumes.
- Reduces context switches.
- Many applications integrated with libgfapi (qemu, samba, NFS Ganesha).
- Both sync and async interfaces available.
- C and python bindings.
- Available via 'glusterfs-api*' packages.

---
NFS-Ganesha

---
NFS access
Why NFS:
  - Widely used network protocol
  - Many enterprises still heavily depend on NFS to access their data from different operating systems and applications.
Native NFS (referred as Gluster-NFS):
  - Acts as GlusterFS client residing on the same node as the GlusterFS server.
  - Supports only NFSv3 protocol
  - Not strictly protocol-complaint

---
NFS-Ganesha
- A user-space, protocol-complaint NFS file server
- Supports NFS v3, 4.0, 4.1, pNFS and 9P from the Plan9 operating system.
- Provides a FUSE-compatible File System Abstraction Layer(FSAL) to plug in to any own storage mechanism
- Can provide simultaneous access to multiple file systems.
  Active participants:
- CEA, Panasas, Red Hat, IBM, LinuxBox

---
Benefits	of NFS-Ganesha
- Dynamically export/unexport entries using D-Bus mechanism.
- Can manage huge meta-data and data caches
- Can act as proxy server for NFSv4
- Provides better security and authentication mechanism for enterprise use
- Portable to any Unix-like file-systems
- Easy access to the services operating in the user-space (like Kerberos, NIS, LDAP)
[Speaker Notes: Running in User Space makes many things easier. – Security Managers (like Kerberos) reside in User Space, they can be accessed directly via GSSAPI (no need for “rpc_pipefs”) – ID mappers (NIS, LDAP) reside in User Space, they can be accessed directly (the daemon is linked with libnfsidmap) – Less constraints for memory allocation than in kernel space, managing huge pieces of memory is easy – When developing in User Space, you won't (usually) crash the kernel]

---
Modular Architecture
- RPC Layer: implements ONC/RPCv2 and RPCSEC_GSS (based on libntirpc)
- FSAL: File System Abstraction Layer, provides an API to generically address the exported namespace
- Cache Inode: manages the metadata cache for FSAL. It is designed to scale to millions of entries
- FSAL UP: provides the daemon with a way to be notified by the FSAL that changes have been made to the underlying FS outside Ganesha. These information is used to invalidate or update the Cache Inode.
[Speaker Notes: Memory allocation and management: NFS-Ganesha do not rely on malloc/free but allocates a big chunck of memory at startup and manages it on its own. This is done by using pre-allocated structures and blocks of memory managed as “Buddy Blocks” Hash Table: provides a Red-Black Tree based hash table to provide associative addressing to internal structure. This layer is widely used to build various cache, including the metadata cache. FSAL UP / Cache Inode UP: provides the daemon with a way to be notified by the FSAL that changes have been made to the underlying FS outside Ganesha. These information is used to invalidate or update the Cache Inode. Each layer has a well defined API. It can be modified (e.g. to implement a different cache policy) without impacting the other modules]

---
NFS-Ganesha Architecture
Admin
DBUS
Network Forechannel
Network
Backchannel
RPC Dispatcher
Dup Req
RPC Sec GSS
NFSv3, NFSv4.x/pNFS,
RQUOTA, 9P
Cache Inode
SAL
FSAL
FSAL_UP
Backend (POSIX, VFS, ZFS,
GLUSTER, GPFS, LUSTRE )

---
NFS-Ganesha + GlusterFS
NFS-Ganesha
Cache Inode
SAL
FSAL_GLUSTER
libgfapi
GlusterFS Volume
GlusterFS
Brick
GlusterFS
Brick

---
Integration with GlusterFS
Integrated with GlusterFS using 'libgfapi' library
That means,
  - Additional protocol support w.r.t. NFSv4, pNFS
  - Better security and authentication mechanisms for enterprise use.
  - Performance improvement with additional caching

---
Clustered NFS

---
Clustered NFS
Stand-alone systems :
    - are always bottleneck.
    - cannot scale along with the back-end storage system.
    - not suitable for mission-critical services
Clustering:
    - High availability
    - Load balancing
    - Different configurations:
        - Active-Active
        - Active-Passive

---
Challenges Involved
  - Cluster wide change notifications for cache invalidations
  - Coordinate Grace period across nodes in the cluster
  - Maintain and recover lock, share reservation and delegations state
  - Provide “high availability” to stateful parts of NFS
    - Share state across the cluster to allow failover
    - IP Failover in case of node failure
    - Lock recovery in case of node failure

---
Active-Active HA solution on GlusterFS
Primary Components
    - Pacemaker
    - Corosync
    - PCS
    - Resource agents
    - HA setup scipt ('ganesha-ha.sh')
    - Shared Storage Volume
    - UPCALL infrastructure

---
Clustering Infrastructure
- Using Open-source services
- Pacemaker: Cluster resource manager that can start and stop resources
- Corosync: Messaging component which is responsible for communication and membership among the machines
- PCS: Cluster manager to easily manange the cluster settings on all nodes

---
Cluster Infrastructure
Resource-agents : Scripts that know how to control various services.
- New resource-agent scripts added to
    - ganesha_mon: Monitor NFS service on each node & failover the Virtual IP
    - ganesha_grace: Puts entire cluster to Grace
- If NFS service down on any of the nodes
    - Entire cluster is put into grace via D-bus signal
    - Virtual IP fails over to a different node (within the cluster).

---
HA setup script
- Located at /usr/libexec/ganesha/ganesha-ha.sh.
- Sets up, tears down and modifies the entire cluster.
- Creates resource-agents required to monitor NFS service and IP failover.
- Integrated with new Gluster CLI introduced to configure NFS-Ganesha.
- Primary Input: ganesha-ha.conf file with the information about the servers to be added to the cluster along with Virtual IPs assigned, usually located at /etc/ganesha.

---
Upcall infrastructure
A generic and extensible framework.
    - used to maintain states in the glusterfsd process for each of the files accessed
    - sends notifications to the respective glusterfs clients in case of any change in that state.
- Cache-Invalidation: Needed by NFS-Ganesha to serve as Multi-Head
  Config options:
    #gluster vol set <volname> features.cache-invalidation on/off
    #gluster vol set <volname> features.cache-invalidation-timeout <value>

---
Shared Storage Volume
- Provides storage to share the cluster state across the NFS servers in the cluster
- This state is used during failover for Lock recovery
- Can be created and mounted on all the nodes using the following gluster CLI command -
  #gluster volume set all cluster.enable-shared-storage enable

---
Clustered NFS-Ganesha
Shared Storage Volume
Node A
Node B
Node C
Node D
Clustering Infrastructure
(Pacamaker/Corosync)
NFS-Ganesha service
Virtual IP
ganesha_mon
ganesha_grace

---
Clustered NFS-Ganesha
Shared Storage Volume
Node A
Node B
Node C
Node D
Clustering Infrastructure
(Pacamaker/Corosync)
NFS
Client
NFS-Ganesha service
Virtual IP
ganesha_mon
ganesha_grace

---
Clustered NFS-Ganesha
Shared Storage Volume
Node A
Node B
Node C
Node D
Clustering Infrastructure
(Pacamaker/Corosync)
NFS
Client
NFS-Ganesha service
Virtual IP
ganesha_mon
ganesha_grace

---
Clustered NFS-Ganesha
Shared Storage Volume
Node A
Node B
Node C
Node D
In Grace
Clustering Infrastructure
(Pacamaker/Corosync)
NFS
Client
NFS-Ganesha service
Virtual IP
ganesha_mon
ganesha_grace

---
Clustered NFS-Ganesha
Shared Storage Volume
Node A
Node B
Node C
Node D
In Grace
Clustering Infrastructure
(Pacamaker/Corosync)
NFS
Client
NFS-Ganesha service
Virtual IP
ganesha_mon
ganesha_grace

---
Step-by-step guide

---
Required Packages
Gluster RPMs (>= 3.7)
    - glusterfs-server
    - glusterfs-ganesha
Ganesha RPMs (>= 2.2)
    - nfs-ganesha
    - nfs-ganesha-gluster
Pacemaker & pcs RPMs

---
Pre-requisites
  - Ensure all machines are DNS resolvable
  - Disable and stop NetworkManager service, enable and start network service on all machines
  - Enable IPv6 on all the cluster nodes.
  - Install pacemaker pcs ccs resource-agents corosync
    - #yum -y install pacemaker pcs ccs resource-agents corosync` on all machines
  - Enable and start pcsd on all machines
    - #chkconfig --add pcsd; chkconfig pcsd on; service pcsd start
  - Populate /etc/ganesha/ganesha-ha.conf on all the nodes.

---
Pre-requisites
  - Create and mount the Gluster shared volume on all the machines
  - Set cluster auth password on all machines
    #echo redhat | passwd --stdin hacluster
    #pcs cluster auth on all the nodes
  - Passwordless ssh needs to be enabled on all the HA nodes.
    - On one (primary) node in the cluster, run:
      #ssh-keygen -f /var/lib/glusterd/nfs/secret.pem
    - Deploy the pubkey ~root/.ssh/authorized keys on _all_ nodes, run:
      #ssh-copy-id -i /var/lib/glusterd/nfs/secret.pem.pub root@$node

---
Sample 'ganesha-ha.conf'
# Name of the HA cluster created. must be unique within the subnet
HA_NAME="ganesha-ha-360"
# The gluster server from which to mount the shared data volume.
HA_VOL_SERVER="server1"
# The subset of nodes of the Gluster Trusted Pool that form the ganesha HA cluster.
# Hostname is specified.
HA_CLUSTER_NODES="server1,server2,..."
#HA_CLUSTER_NODES="server1.lab.redhat.com,server2.lab.redhat.com,..."
# Virtual IPs for each of the nodes specified above.
VIP_server1="10.0.2.1"
VIP_server2="10.0.2.2"

---
Setting up the Cluster
New CLIs introduced to configure and manage NFS-Ganesha cluster & Exports
#gluster nfs-ganesha <enable/disable>
    - Disable Gluster-NFS
    - Start/stop NFS-Ganesha services on the cluster nodes.
    - Setup/teardown the NFS-Ganesha cluster.
#gluster vol set <volname> ganesha.enable on/off
    - Creates export config file with default parameters
    - Dynamically export/unexport volumes.

---
Modifying the Cluster
- Using HA script ganesha-ha.sh located at /usr/libexec/ganesha.
- Execute the following commands on any of the nodes in the existing NFS-Ganesha cluster
- To add a node to the cluster:
    #./ganesha-ha.sh --add <HA_CONF_DIR> <HOSTNAME> <NODE-VIP>
- To delete a node from the cluster:
    #./ganesha-ha.sh --delete <HA_CONF_DIR> <HOSTNAME>
    Where, HA_CONF_DIR: The directory path containing the ganesha-ha.conf file.
      HOSTNAME: Hostname of the new node to be added
      NODE-VIP: Virtual IP of the new node to be added.

---
Modifying Export parameters
 On any of the nodes in the existing ganesha cluster:
  - Edit/add the required fields in the corresponding export file located at /etc/ganesha/exports.
  - Execute the following command:
    #./ganesha-ha.sh --refresh-config <HA_CONFDIR> <Volname>
      Where,
      - HA_CONFDIR: The directory path containing the ganesha-ha.conf file
      - Volname: The name of the volume whose export configuration has to be changed.

---
Next

---
 pNFS (Parallel Network File System)
- Introduced as part of NFSv4.1 standard protocol
- Needs a cluster consisting of M.D.S. (meta data server ) and D.S. (Data server)
- Any filesystem can provide pNFS access via NFS-Ganesha by means of the FSAL easy plugin architecure
- Support for pNFS protocol ops added to FSAL_GLUSTER (in NFS-Ganesha V2.2)
- Currently supports only FILE LAYOUT

---
Future Directions
- NFSv4 paves the way forward for interesting stuff
- Adding NFSv4.x feature support for GlusterFS
    - Directory Delegations
    - Sessions
    - Server-side copy
    - Application I/O Advise (like posix_fadvise)
    - Sparse file support/Space reservation
    - ADB support
    - Security labels
    - Flex File Layouts in pNFS

---
Contact
Mailing lists:
    - nfs-ganesha-devel@lists.sourceforge.net
    - gluster-users@gluster.org
    - gluster-devel@nongnu.org
IRC:
    - #ganesha on freenode
    - #gluster and #gluster-dev on freenode
    - team: Apeksha, ansubram, jiffin, kkeithley, meghanam, ndevos, saurabh, skoduri

---
References & Links
Links (Home Page):
    - https://github.com/nfs-ganesha/nfs-ganesha/wiki
    - http://www.gluster.org
References:
    http://gluster.readthedocs.org
    http://blog.gluster.org/http://www.nfsv4bat.org/Documents/ConnectAThon/2012/NFS-GANESHA_cthon_2012.pdfhttp://events.linuxfoundation.org/sites/events/files/slides/Collab14_nfsGanesha.pdfhttp://www.snia.org/sites/default/files/Poornima_NFS_GaneshaForClusteredNAS.pdf
    http://clusterlabs.org/doc/

---
Q & A

---
Thank you!
Soumya Koduri
Meghana Madhusudhan